## Slide 1: What are Floods?
When the river’s discharge exceeds the carrying capacity of the channel a river will flood. The water level then rises above the banks and spreads onto the floodplains.

## Slide 3
Construction
And
Analysis of Hydrographs

## Slide 4
Hydrograph
Record of River Discharge over a period of time
River Discharge
= cross sectional area
rivers mean velocity
X
(at a particular point in its course)

## Slide 5
Why
Construct & Analyse Hydrographs ?
To find out discharge patterns of
  a particular drainage basin
Help predict flooding events,
  therefore influence implementation of flood prevention measures

## Slide 6
0 12 24 36 48 60 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)

## Slide 7
0 12 24 36 48 60 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
mm
4
3
2
Rainfall shown in mm, as a bar graph

## Slide 8
0 12 24 36 48 60 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
mm
4
3
2
Discharge in m3/s, as a line graph

## Slide 9
0 12 24 36 48 60 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
mm
4
3
2
Rising limb
The rising flood water in the river

## Slide 10
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
mm
4
3
2
Peak flow
Peak flow
Maximum discharge in the river

## Slide 11
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
Recession limb
mm
4
3
2
Peak flow
Recession limb
Falling flood water in the river

## Slide 12
0 12 24 36 48 60 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Rising limb
Recession limb
Basin lag time
mm
4
3
2
Peak flow
Basin lag time
Time difference between the peak of the rain storm and the peak flow of the river

## Slide 13
0 12 24 36 48 60 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
Base flow
Through flow
Overland flow
Rising limb
Recession limb
Basin lag time
mm
4
3
2
Peak flow
+
=
Storm Flow
Overland Flow
Volume of water reaching the river from surface run off
Through Flow
Volume of water reaching the river through the soil and underlying rock layers

## Slide 14
Analysis

## Slide 15
When interpreting hydrographs all factors must be considered together !
Here are some theoretical interpretations of influencing factors
BUT……

## Slide 16
Factors influencing
Storm Hydrographs
Area
Shape
Slope
Rock Type
Soil
Land Use
Drainage Density
Precipitation / Temp
Tidal Conditions

## Slide 17
Area
Large basins receive more precipitation than small therefore have larger runoff
Larger size means longer lag time as water has a longer distance to travel to reach the trunk river
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 18
Shape
Elongated basin will produce a lower peak flow and longer lag time than a circular one of the same size
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 19
Slope
Channel flow can be faster down a steep slope therefore steeper rising limb and shorter lag time
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 20
Rock Type
Permeable rocks mean rapid infiltration and little overland flow therefore shallow rising limb
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 21
Soil
Infiltration is generally greater on thick soil, although less porous soils eg. clay act as impermeable layers
The more infiltration occurs the longer the lag time and shallower the rising limb
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 22
Land Use
Urbanisation - concrete and tarmac form impermeable surfaces, creating a steep rising limb and shortening the time lag
Afforestation - intercepts the precipitation, creating a shallow rising limb and lengthening the time lag
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 24
Drainage Density
A higher density will allow rapid overland flow
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 25
Precipitation & Temperature
Short intense rainstorms can produce rapid overland flow and steep rising limb
If there have been extreme temperatures, the ground can be hard (either baked or frozen) causing rapid surface run off
Snow on the ground can act as a store producing a long lag time and shallow rising limb. Once a thaw sets in the rising limb will become steep
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 26
Tidal Conditions
High spring tides can block the normal exit for the water, therefore extending the length of time the river basin takes to return to base flow
Area Rock Type Drainage Density
Shape Soil Precipitation / Temp
Slope Land Use Tidal Conditions

## Slide 27
Factors influencing
hydrographs

## Slide 28
Remember!
These influencing factors will:
Influence each other
Change throughout the rivers course
©Microsoft Word clipart

## Slide 29
Made by:
Steven Heath